## Slide 1
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
N
H
H
H
2D mathematical model study of a packed bed membrane reactor for ammonia synthesis: optimization, design and scale-up
I. Gargiulo, A.E. Simpelaar, E. A.J.F. Peters, F. Gallucci
Sustainable Process Engineering – Chemical Engineering and Chemistry – Eindhoven University of Technology

## Slide 2
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
2
Catalytic membrane reactor
for in-situ removal of NH3
Effective heat management
Energy efficiency
Process intensification
Target conditions:
T=250-300 °C
P=20 bar
Shifting the equilibrium towards products
(Le Chatelier’s principle)
NH3 in packed bed membrane reactor
Renewable
energy
Ammonia
synthesis
Ammonia transport
and storage
Ammonia
decomposition
Ammonia direct
utilization
Hydrogen
utilization
NH3
H2
N2

## Slide 3
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
3
Modeling approach
Assumption
Weisz-Prater criterion (CWP): internal mass transfer
Mears criterion (CM):
external mass transfer
Bodenstein number (Bo):
axial dispersion
Neglected
Neglected
Neglected
Reynold-Schmidt number (ReSc):
radial diffusion
Depending on the axial velocity, it cannot be always neglected

## Slide 4
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
4
Modeling approach
Model equations
Partial continuity equation: mass balance
Partial continuity equation: energy balance
Ergun equation

## Slide 5
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
5
Modeling approach
Boundary conditions
Partial continuity equation: mass balance
Inlet
Membrane wall
Reactor wall
Centre

## Slide 6
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
6
Modeling approach
Boundary conditions
Partial continuity equation: energy balance
Inlet
Membrane wall
Reactor wall
Centre

## Slide 7
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
7
Deviation between 1D and 2D model
Concentration profile in two different case scenario when is still valid
PR=30 bar , GHSV= 21 1/h
PR=5 bar , GHSV= 126 1/h
When using high P, even at low GHSV, there is a bigger concentration gradients, due to the diffusion limitation

## Slide 8
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
8
Optimization of 2D model
Performance factor
Temperature control

## Slide 9
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
9
Optimization of 2D model
Catalyst weight study according to GHSV
Isothermal
Non-Isothermal

## Slide 10
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
10
Optimization of 2D model
  Sweep gas ratio study according to GHSV

## Slide 11
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
11
Optimization of 2D model
  What about SW composition?
When there is only N2, outlet temperature is lower, due to the higher heat capacity
Important to keep the temperature profile constant and low, for the membrane selectivity

## Slide 12
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
12
Optimization of 2D model
  Retentate and permeate temperature study

## Slide 13
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
13
Optimization of 2D model
  Optimized reactor conditions

## Slide 14
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
14
Design and scale-up
 | Lmem (m) | DR (m)
Geometry 1 | 0.2 | 0.05133
Geometry 2 | 0.95 | 0.05133
Geometry 1(X5) | 1.0 | 0.05133
Geometry 1 (X6) | 1.2 | 0.05133
  Length influence study
Membrane
Reactor

## Slide 15
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
15
Design and scale-up
 | Total membrane length [m] | Production capacity [g/hr] | Purity [%] | Catalyst weight [g]
Geometry 1 | 0.95 | 68.4 | 45.3 | 235
Geometry 2 | 0.2 | 12.5 | 34.3 | 35
Geometry 2 (X5) | 1.0 | 62.5 | 34.3 | 175
Geometry 2 (X6) | 1.2 | 75 | 34.3 | 210
  Length influence study
Catalyst mass in geometry 2 with 6 short reactors is lower than one single membrane reactor with geometry 1
At the same time the production capacity is higher

## Slide 16
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
16
Design and scale-up
  Diameter influence study
At 1 cm production capacity is already 45 g/hr, and with a four-time distance this is increased about 62%.
At the same time more catalyst is needed

## Slide 17
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
17
Design and scale-up
  Cooling strategy: reaction profiles
No wall cooling
TW=TIN=653 K
TW=TAVE=683 K
Fast reaction at the membrane wall, very slow at reactor wall
Reaction slow everywhere
Faster reaction at the bottom because the gas is heated by the wall
Using lower Temperature would decrease too much the reaction rate

## Slide 18
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)
18
Conclusions
2D model was successfully implemented and validated with kinetic experimental test from literature and permeation lab experimental test
2D model outperform 1D model even when . This is due to the diffusion limitation
Optimal membrane reactor conditions were found
Reactor length study showed the advantage to have a multitube membrane reactor in terms of catalyst mass
Reactor diameter study showed most likely the best membrane distance in a multitube reactor should be between 1 and 2 cm
Cooling strategy study showed too much lower temperature slow down the kinetic

## Slide 19: Thank you for the attention! Questions??
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 101058565 (Ambher project).
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union. Neither the European Union nor the granting authority can be held responsible for them
3rd SYMPOSIUM on AMMONIA ENERGY, Sep 23-26 2024, Shanghai (China)